## Slide 1: Case Studies for Sustainability Metrics and Sustainability Footprint method
Debalina Sengupta
Artie McFerrin Department of Chemical Engineering
Texas A&M University

## Slide 2: Overview
Fender Case
Auto Shredder Residue (ASR) Case
Biodiesel Case

## Slide 3: Fender Case Study
The first case analyzed here involves comparing five different automobile fenders made of steel, aluminum, and three different plastics formulations (Saur et al. 2000).
Twelve indicators including energy, water, and resource use, as well as waste and emissions generated were used to compare the different options.
Saur C, Fava J, and Spatari S (2000) Life cycle engineering case study: automobile fender designs. Env Prog 19(2):72–82

## Slide 4: Fender Case Study
Economic Aspects
Social Aspects
Environmental Aspects
Ecotox
Htox air
Htox water
Socio-Economic Metrics
Water
GWP
ODP
AP, EP, POCP,
waste
Socio-Ecological Metrics
Energy, Resources
Mapping the accepted metrics on the Venn diagram would tell us if all sustainability considerations have been covered. This inspection may trigger looking for additional metrics or weed out the redundant one.

## Slide 5
Chart: 
| energyx10(-3) | resourcesx10(-1) | waterx10(-1) | GWPx10(-2) | ODP | APx10(-1) | EP | POCP | Htox air | Htox water | Eco tox | waste
Al | 1.29 | 1.5 | 3.6 | 1.04 | 1 | 2.8 | 4.4 | 6.7 | 3.8 | 0.66 | 2.9 | 3.7
St | 1.12 | 2.5 | 2.7 | 1.05 | 0.1 | 1.9 | 4.2 | 9.2 | 3.7 | 0.92 | 3.4 | 1.2
PC/PBT | 1.06 | 1.8 | 2.2 | 0.83 | 0.4 | 2 | 3.9 | 8.7 | 2.5 | 0.99 | 2.7 | 1
PP/ EPDM | 0.81 | 1.4 | 1.7 | 0.62 | 0.2 | 1.6 | 3.5 | 8 | 1.9 | 0.62 | 1.9 | 0.25
PPO/PA | 1.08 | 2.1 | 2.5 | 1.15 | 1.2 | 2 | 7.2 | 9.1 | 2.5 | 0.74 | 2.4 | 0.25
Fender Case Study: comparison of the alternatives

## Slide 6: Fender Case Study

## Slide 7
Chart: 
| Al | St | PC/PBT | PP/EPDM | PPO/PA
 | 2.6117 | 2.466 | 1.7025 | 0.52789 | 2.2907
Fender Case Study
Comparison of the alternatives with De
Best Option, Lowest De

## Slide 8: Automotive Shredder Residue Case Study
We first encountered negative values of indicators in an interesting case of sustainably managing automotive shredder residues (Vermeulen et al. 2012).
Four process options to consider for recommending the option that is the most sustainable among the options:
  (1) landfilling,
  (2) recycling the metal values coupled with landfilling the rest,
  (3) energy recovery, and
  (4) recycling metal values and recovering energy from the rest.
  Nine metrics, all normalized to one metric ton of automotive shredder residue, for comparative sustainability analysis of these four process options:
  (1) energy intensity,
  (2) material intensity,
  (3) water consumption,
  (4) land use,
  (5) short-term global warming potential,
  (6) long-term global warming potential,
  (7) short-term human toxicity impact,
  (8) long-term human toxicity impact, and
  (9) treatment cost.

## Slide 9
Automotive Shredder Residue Case Study

## Slide 10
Economic Aspects
Total cost
Land use
Social Aspects
Environmental Aspects
GWP (LT, ST)
Human toxicity (ST, LT)
Water
Socio-Ecological Metrics
Energy, Material
Automotive Shredder Residue Case Study

## Slide 11
Automotive Shredder Residue Case Study

## Slide 12: Automotive Shredder Residue Case Study
The PLS-VIP score shows that Total Cost (TC) has the maximum contribution to overall sustainability.
TC, HTST, HTLT, WC, MI, and GWLT have values higher than VIP score of 1.0. Using 1.0 as the cutoff point, three indicators, namely LU, EI, and GWST are less than significant and can be excluded from analysis.
Chart: Indicator
| TC | HTST | HTLT | WC | MI | GWLT | LU | EI | GWST
VIP | 1.1004 | 1.0966 | 1.065 | 1.0442 | 1.0065 | 0.99372 | 0.92636 | 0.88996 | 0.84345
 | 1 | 1

## Slide 13: Biodiesel Case Study
Example of indicators where higher value means good. Converted to fraction such that lower value is good.
Example of missing data. Data substitution by taking mean of other values.

## Slide 14: Biodiesel Case Study
De is used to compare the several options. The process with the lowest De is the most acceptable.
Debalina Sengupta, Rajib Mukherjee and Subhas K. Sikdar, Chapter 4 - Moving to a decision point in sustainability analyses, In Assessing and Measuring Environmental Impact and Sustainability, edited by Jiří Jaromír Klemeš, Butterworth-Heinemann, Oxford, 2015, Pages 87-129, ISBN 9780127999685