## Slide 1: Decision Making with Metrics and Indicators
Debalina Sengupta
Artie McFerrin Department of Chemical Engineering
Texas A&M University

## Slide 2: Overview
Backgroud
Metrics and Indicators requirements
The Sustainability Footprint Method
  Unidirectional Data
  Aggregate Index for computing single value
  PLS-VIP for computing importance of indicators

## Slide 3
Range of scores
Average
AIChE SI 2009 Results Overview

## Slide 4
BASF Eco-efficiency analysis: combines Environmental and Economic Dimensions of Sustainability
BASF Sustainability Analysis: combines all three dimensions of sustainability (called socio-eco-efficiency)
Chart: 
| toxicity potential | energy | emissions and waste | raw materials | process risk | land area
 | 7 | 5 | 4 | 5 | 6 | 1
 | 9 | 3 | 6 | 3 | 5 | 8
BASF Eco-Efficiency Analysis and the SEEBALANCE Method

## Slide 5: Properties for good Metrics or Indicators
Indicators:
Should be selected to measure changes in all three sustainability domains
If possible, they should be orthogonal
Redundancy should be avoided
Only necessary and sufficient number of indicators should be selected
Typically when a process or a product is developed for a beneficial end result, some key indicators are shown to have improved with respect to a current practice without a comprehensive comparative analysis. Often it involves energy use and GHG emission, perhaps even water use.
Multiple indicators are used ideally representing all three Bruntland dimensions for a comparative analysis.

## Slide 6
Process options (m) | Process Indicators (n) |  |  |  |  |  |  |  | 
 | X1 | X2 | X3 | X4 | X5 | X6 | X7 | X8 | X9
Option 1 | X1,1 | X1,2 | .. | .. | .. | .. | .. | .. | X1,9
Option 2 | X2,1 | X2,2 | .. | .. | .. | .. | .. | .. | X2,9
Option 3 | X3,1 | X3,2 | .. | .. | .. | .. | .. | .. | X3,9
Option 4 | X4,1 | X4,2 | .. | .. | .. | .. | .. | .. | X4,9
Option 5 | X5,1 | X5,2 | .. | .. | .. | .. | .. | .. | X5,9
Option 6 | X6,1 | X6,2 | .. | .. | .. | .. | .. | .. | X6,9
Option 7 | X7,1 | X7,2 | .. | .. | .. | .. | .. | .. | X7,9
Typical Data Matrix for m options and n indicators

## Slide 7: An Alternative Way for Decision Making via Aggregate Index
Single Index: Easy decision making capability with a single aggregate index, when computed in an unbiased fashion
Vs.
For table of data or spider diagram: Difficulty of decision making from tables of data or use of a spider diagram, especially when contenders or number of indicators are large.
Eco services indicator is a qualitative composite of 8 indicators: crop production, forest production, preserving habitats and biodiversity, water flow regulation, water quality regulation, carbon sequestration, regional climate and air quality regulation, infectious disease mediation

## Slide 8: Sustainability Footprint Method
Step 1: Ensure Quality and Unidirectionality of Indicator Data
Step 2: Compare Relative Sustainability of Options: The Aggregate Index Method for Sustainability Footprint
Step 3: Compare the Ranking of Indicators: Partial Least Square-Variable Importance in Projection Method

## Slide 9: Step 1: Ensure Quality and Unidirectionality of Indicator Data
QUALITY
Data deletion: Omitting entire records (for indicators or system options) when substantial data are missing. Deleting data entirely for an option takes that option out of consideration, however.
Mean substitution: This method takes the average of the remaining values of the same indicator, thus substituting a mean value computed from the other options available to fill in missing values. This can be used for temporal data.
Regression: Using regressions based on other indicators to estimate the missing values. This is useful when temporal data on indicators are missing for a certain option.
Nearest neighbor: Identifying and substituting the most similar case for the one with a missing value.
Ignore value: This is essentially assuming a numerical value of zero for the indicator. Care must be taken here to confirm that ignoring the value is physically consistent, i.e. the indicator is actually zero. Otherwise some of the other methods above should be applied.
UNIDIRECTIONAL
Unidirectional: Apply mathematical modifications such that all the indicators are unidirectional, i.e. a smaller value represents a better option and higher value is a worse option
  1/Value if number
  100-Value if percentage
  -1*Value if negative/positive

## Slide 10: Step 2: Compare Relative Sustainability of Options
The aggregate index computation involves two parts:
normalization of the indicators
  Based upon the Distance from the best and worst performers, where positioning is in relation to the maximum and minimum in the data set and the index takes values between 0 and 1 (or 100%):
computation of the aggregate index
De (t, xj) is relative sustainability of an option m from a designated reference n dimensional point
xj is the value of jth indicator for option m (process, product etc.)
xjo is the value of jth indicator for the reference point
cj is the weighting factor for jth indicator
n is the number of indicators used

## Slide 11: Step 3: Compare the Ranking of Indicators
Partial Least Squares Regression (PLS) model is used to decompose the original data matrix X into two orthogonal matrices, the loadings (L) and scores (T) of a number of latent indicators, and a residual matrix, E
The score matrix T is related to the response vector De through a regression matrix b
Values of the indicator for each option are represented as an option vector xm. Each option vector xm can be related to the score vector through weight vectors wj
Variable Importance in Projection (VIP) for a particular indicator, is calculated using the regression coefficient b, weight vector wj and score vector tj

## Slide 12: Use of De in Determining Relative Sustainability
Decision Point 1
When the number of metrics is small and supposedly independent,
a. The aggregate index can be used for pairwise comparison of any number of comparable cases (time as a variable is unimportant).
b. The same system can be tracked through time.
Decision Point 2
When the number of metrics is large,
a. Use of the Principle Component analysis along with Partial Least Squares and Variable Importance in Projection (PLS-VIP) to provide the necessary and sufficient number of metrics.
b. PCA checks for metric redundancy, and PLS-VIP uses De to provide metrics sufficiency as well as the order of their importance in representing the system.
Notes: One can make decisions after 1. If we want to know more, such as are some of the used indicators redundant? What is the order of importance of the indicators with respect to the sustainability outcome?

## Slide 13: Concluding Remarks
Aggregate Index in Sustainability Footprint method provides unique decision point for multiple indicator systems
It allows for negative values of indicators
PLS-VIP method helps to rank indicators in order of importance