## Slide 1: Sustainability Metrics and Indicators for Sustainable Manufacturing
Debalina Sengupta
Artie McFerrin Department of Chemical Engineering
Texas A&M University

## Slide 2: Overview
Sustainability Considerations
  Axioms
  Systems Analysis
  Scale of Systems
Metrics and Indicators
  Types of metrics
  Computing metrics

## Slide 3: Axioms for Sustainability Considerations
Sustainability is about systems
Sustainability is always relative, never absolute
Sustainability functions (economic, environmental, and societal) of systems are described by a parsimonious set of indicators
Scale of the system determines the nature of the set of indicators and the sustainability analysis
Indicators are not pure (in Bruntland sense); they are often two or three dimensional

## Slide 4: System-Surrounding Paradigm
System: maximum space over which the process owner has control
Sustainability Analysis: essentially an accounting of what the system is doing to itself and to the surrounding in terms of environmental, societal, and economic impacts, and how these impacts can be minimized

## Slide 5: Systems View of Sustainability
Environment (natural capital)
waste and emissions may degrade the environment
ecological goods and services are utilized in industry
ecological goods and services are utilized in society
some waste is recovered and recycled
emissions may harm humans
Society
(human capital)
Economy
(economic capital)
economic value is created for society

## Slide 6: Sustainability: Systems Analysis
Must be comparative to a reference system
Must be based on life cycle of material, energy, and cost through the appropriate supply chain
Must consider quantitative measure to represent environmental, economic, and societal domains
Must identify the necessary and sufficient number of critical metrics that characterize the system
Must lead to a decision of better or worse than the reference system, preferably with a single aggregate metric (or index)

## Slide 7: Scale of Systems
Type I: Global Systems (e.g. global CO2 budgeting)
Type II: Systems bounded by geographical boundaries, such as National Systems (energy system, material flow) and Regional Systems (e.g. watersheds, Brownfields)
Type III: Business Systems (e.g. business networks, waste exchange networks)
Type IV: Sustainable technologies (e.g. green materials, sustainable products)
III: Business or Institutional Scale (e.g. eco-industrial park)
IV: Sustainable Technologies Scale
(e.g. sustainable products)
II. National Scale (e.g. energy) and Regional Scale (e.g. watersheds, epa regions)
I: Global Scale
(e.g. global CO2 budgeting)

## Slide 8: Different Goals for Each System!
Global Systems: Sustainable planet
Regional: Sustainable Ecosystems, Sustainable City, Economic Sustainability, Environmental Sustainability, Societal Sustainability, Sustainable Water
Institutional: Sustainable Corporation, Sustainable Industry, Sustainable Energy
Technology: Sustainable Product, Sustainable Process

## Slide 9: Sustainability for Manufacturing
The 6-R concept for Sustainable Manufacturing
Jayal, A. D., et al. "Sustainable manufacturing: Modeling and optimization challenges at the product, process and system levels." CIRP Journal of Manufacturing Science and Technology 2.3 (2010): 144-152.

## Slide 10: Sustainable Manufacturing
Environmental Friendliness
Manufacturing Cost
Power Consumption
Waste Management
Operational Safety
Personal Health
Sustainable Manufacturing
Processes
Metrics and indicators provide the “looking glass” for evaluating the sustainability of Manufacturing Processes

## Slide 11: Engineering Approaches to Sustainability
Impact accounting: on a life cycle basis
Analysis: comparative among processes, or over time
Reference system: the one to supersede or a chosen synthetic
Applicable metrics: to be used in the comparative study
Reference system
System Option 1
System Option 2
System Option n
…
…
System Option 1
LC Stage 1 LC Stage 2 LC Stage 3 LC Stage 4
System Option 1
Year 1 Year 2 Year 3 Year 4
Metrics
Metrics
Metrics
Impact
accounting
Analysis

## Slide 12: Sustainability: Intersection of three domains
Economic Aspects
Social Aspects
Environmental Aspects
Socio-Economic Metrics
Eco-efficiency Metrics
Socio-Ecological Metrics
Sustainability Metrics
Metrics Classification:
1-D Metrics: Economic, Environmental, Social
2-D Metrics: Eco-efficiency Socio-Economic, Socio-Ecological
3-D Metrics: Sustainability

## Slide 13: Examples
Capital Cost
Operating Cost
1-D
Employment
Disease
1-D
Biodiversity
1-D
Cost/Benefit
Water use
Waste
GHG
Land use
energy intensity
material intensity
chemical risk
environmental risk
2-D
2-D
2-D
3-D

## Slide 14: Common Sustainability Measures
Product and Processes from Chemical and Allied Industries
(3D) Energy Consumption and its impacts
(3,2,1 D) Water Consumption
(3D) Non-Water Material Consumption and its impacts
Unit Cost (2D)
Wastes, emissions, recyclability, treatment etc. (2D)
Health Impacts
Eco Impacts (2D)
Product(s)
And
LCA-based impacts
INPUTS
IMPACTS

## Slide 15: Core and Supplemental Indicators for Sustainability Assessment of Chemical Processes
Core Indicators Supplemental Indicators
Energy Use renewable energy, recovery, etc.
Material Use restricted materials, in-process recycled
Fresh water use in-process, recycled
Land use biodiversity loss, adverse impacts
Waste intensity treated, recycled, valorization
Pollution intensity human and eco-toxicological, treatment
Cost liability cost, treatment cost
Emissions from use biodegradability, persistence, etc.
Process Safety inherency of chemical safety
(at the plant level, additional indicators, such as child labor, worker rights, etc. will be needed)

## Slide 16: AIChE’s Center for Waste Reduction Technologies (CWRT) metrics for chemical processes
Output: Mass of Product or Sales Revenue or Value-Added | Material Intensity
 | Water Intensity
 | Energy Intensity
 | Solid Waste to Landfill
 | Toxic Release
Basic sustainability metrics

## Slide 17: AIChE’s Center for Waste Reduction Technologies (CWRT) metrics for chemical processes
Indicator | Metric for measuring the indicator
Material | Packaging materials Non-renewable materials Toxics in product Toxics in raw materials
Water | Rainwater sent to treatment Water from endangered ecosystem sources Water use relative to water availability
Energy | Energy consumed in transportation Non-renewable energy
Solid waste | Solid waste disposed relative to landfilling capacity
Toxic release | Toxic release under each TRI category Human toxicity (carcinogenic) Human toxicity (non-carcinogenic) Ecosystem toxicity
Pollutant effects | Global warming potential Tropospheric ozone depletion potential Photochemical ozone creation potential Air acidification potential Eutrophication potential

## Slide 18: IChemE Sustainability Metrics
ENVIRONMENTAL - RESOURCES
energy material water land
ENVIRONMENTAL - IMPACTS
acidification global warming human health ozone depletion photochemical ozone wastes – hazardous, nonhazardous ecological health

## Slide 19: IChemE Sustainability Metrics
  ECONOMIC METRICS
  value added
  value added per unit value of sales
  value added per direct employee
  gross margin per direct employee
  return on average capital employee
  percent increase (decrease) in capital employee
  R&D expenditures as % sales

## Slide 20: IChemE Sustainability Metrics
  SOCIAL METRICS
benefits as percentage of payroll expense
employee turnover
promotion rate
working hours lost as percent of total hours worked
income and benefit ratio (top 10%/bottom 10%)
lost time accident frequency
expenditure on illness and accident prevention/payroll expense
number of complaints per unit value added

## Slide 21: Pharma industry eco-efficiency indicator sets
  Global warming
  Ozone depletion
  Material intensity
  Toxic release
  Energy intensity
  Water intensity
  Product characteristics
  Quality of management

## Slide 22: BASF Eco-efficiency Indicators for Products
  Raw materials Use
  Energy Use
  Water use
  Toxicity potential
  Emissions and waste
  Land use

## Slide 23: How to Compute Indicator Values?
Product and Processes from Chemical and Allied Industries
INPUTS
OUTPUTS
Main Product
Co-Product
Solid Waste
Waste Water
Air Pollutants
Toxic Releases
…
…
…
Raw Materials
Water (fresh or recycled)
Electricity
Energy (natural gas, steam)
…
…
…

## Slide 24: Computing Metrics
The basic metrics are computed from the data collected on the processes, e.g. raw materials, products, environmental releases etc.
It is always important to express metrics in the form of an intensity, such as material or energy intensity which makes it comparable to metrics from another process.
Secondary metrics are those which require further characterization factors to compute and compile several species into a single number.
For example, the Global Warming Potential is an indicator which multiplies characterization factors to green house gas releases and adds these values to get a single indicator for GWP.

## Slide 25: Concluding Remarks
Sustainability Metrics are 1,2 or 3 dimensional
Sustainability Metrics always compare options within systems (relative)
No standard metrics for manufacturing systems
AIChE and IChemE metrics are suitable for use for manufacturing systems